## Slide 1: Screening and diagnostics

## Slide 2: Magnetic resonance elastography (MRE)* is an additional tool available to measure liver stiffness
*LSM obtained from MRE is currently regarded as the most accurate biomarker for non-invasive liver fibrosis evaluation. †The shortened version of MRE may be available at lower cost in some centers. AUROC, area under the receiver operating characteristic curve; F, fibrosis stage; LSM, liver stiffness measurement; MR, magnetic resonance; MRE, magnetic resonance elastography; MRI, magnetic resonance imaging. 1. Chen J et al. Eur Radiol. 2022;32(2):950–958. 2. Loomba R et al. Hepatology. 2014;60(6):1920–1928. 3.Charoenuchue P et al. Diagnostics. 2025;15(62):1-15. 4. Ghadimi M, Thomas A. StatPearls [internet]. Updated May 2025. https://www.ncbi.nlm.nih.gov/books/NBK551669/. Accessed December 2025. 5. Liang J et al. J Hepatol. 2023;79(3):592–604.
Fibrosis stage | ≥F2 | ≥F3 | F4
Definition | Significant fibrosis | Advanced fibrosis | Cirrhosis
Cut-off | 3.14 kPa | 3.53 kPa | 4.45 kPa
Pretest probability | 39.4% | 24.1% | 8.7%
AUROC | 0.92 | 0.92 | 0.94
Sensitivity | 79% | 87% | 88%
Specificity | 89% | 88% | 89%
Additional clinical NITs available
Benefits
Ability to identify fibrosis stage with increased accuracy2
Used in clinical practice and research2
Incorporated into guidelines2
Validated in mixed populations2
Quantitative assessment using MR technology to measure liver stiffness1
Limitations
Higher cost3,†
Dependence on sites that have access to MR scanners and special equipment3
Time consuming2
MRI contraindicated in patients with metallic implants4

## Slide 3: Ultrasound is a commonly used and reliable clinical NIT used to diagnosis steatosis
AUROC 0.93 for liver steatosis 20–30%1
BMI may affect accuracy of results4
Inter- and intra-observer variability1
Can reliably diagnose moderate and severe steatosis but does not exclude lower degrees of steatosis1,*
Commonly used in clinical practice1
Identify steatosis, ascites and masses (e.g., HCC)1-3
*Ultrasound is not recommended for routine use by United States Guidelines. AUROC, area under the receiver operating characteristic curve; BMI, body mass index; HCC, hepatocellular carcinoma. 1. Hernaez R et al. Hepatology. 2011;54(3):1082–1090. 2. Getnet W et al. Ethiop J Health Sci. 2019;29(3):383–390. 3. Hu H et al. J Clin Transl Hepatol. 2024;12(5):516–524. 4. Li Q et al. World J Hepatol. 2018;10(8):530–542.
Ultrasound | Can diagnose steatosis
Ultrasound with elastography (e.g. Fibroscan®) | Can diagnose steatosis and fibrosis
Additional clinical NITs available